## Slide 1
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
Next Steps
Next step is to analyze performance for 64×64 and 256×256matrices to evaluate execution cycle variation with size.
Modify the C code to integrate the provided channel estimation algorithm and satisfy the required system specifications.
KPIs achieved till now
Matrix Multiplication executed for various matrix sizes (1×1, 5×5,16×16)
Peformance was analyzed by observing the number of clock cycles for matrix multipication of varying sizes.
Key Achievements/ Outcome till now
Optimization of matrix multiplication core for various sizes
For matrix size 16×16, the executed output was correct and achieved with the least number of cycles, indicating optimized performance.
Any Challenges/ Issues faced
Execution and display of large matrices in Ubuntu PULP showed errors due to their large size exceeding handling capacity.
Optimization inconsistency across different matrix sizes
Date: 21-04-2025

## Slide 2
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name: Cambridge Institute of Technology Banglore
  Requirement: C compiler (e.g., GCC)), Linux/Windows OS
  Status: C environment setup complete; dataset under review; initial test code compiled and working
Any Anticipated Break (Due to exams etc)
Internals :27-03-2025 To 29-03-2025
Resource Requirement Identified with Status
Is the data self-collected, If yes then is the consent form submitted.
If open source then the dataset link
Data Collection Information
PRISM:Registered
Github Repository Link and PRISM Portal Registration
Status
Date: 21-04-2025

## Slide 3
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
Least Square Estimation Algorithm

## Slide 4
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
ML Channel Estimation Algorithm

## Slide 5
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
Minimum Square Error Algorith

## Slide 6
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006_RISC_V
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
Block Diagram

## Slide 7
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
output for 1*1 matrix multiplication

## Slide 8
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
output for 5*5 matrix multiplication

## Slide 9
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006_RISC_V
College Name:Cambridge Institute of Technology Banglore
Date: 21-04-2025
output for 16*16

## Slide 10
Program for 16*16 matrix multiplication
#include <stdio.h>
#include <riscv_vector.h>
#define SIZE 16
void multiplyMatrices(int firstMatrix[SIZE][SIZE],
int secondMatrix[SIZE][SIZE],
int result[SIZE][SIZE])
{
for (int i = 0; i < SIZE; i++)
{
for (int j = 0; j < SIZE; j++)
{
result[i][j] = 0;
for (int k = 0; k < SIZE; k++)
{
result[i][j] += firstMatrix[i][k] * secondMatrix[k][j];
}
}
}
}void printMatrix(int matrix[SIZE][SIZE])
{
for (int i = 0; i < SIZE; i++)

## Slide 11
{
for (int j = 0; j < SIZE; j++)
{
printf("%5d ", matrix[i][j]);
}
printf("\n");
}
}
int main()
{
int firstMatrix[SIZE][SIZE], secondMatrix[SIZE][SIZE], result[SIZE][SIZE];
// Initializing matrices with sample values
for (int i = 0; i < SIZE; i++)
{
for (int j = 0; j < SIZE; j++)
{ firstMatrix[i][j] = i + j; secondMatrix[i][j] = i - j;
}
}
printf("First Matrix:\n");
printMatrix(firstMatrix);
printf("\nSecond Matrix:\n");
printMatrix(secondMatrix);
multiplyMatrices(firstMatrix, secondMatrix, result);
printf("\nResultant Matrix:\n");
printMatrix(result);
return 0;}

## Slide 12
Program for 16*16 matrix multiplication[alternative]
Worklet ID: CT006_RISC_V
Co
Date: 21-04-2025
#include <printf.h>
#include <riscv_vector.h>
#include <stdint.h>
#include <math.h>
void fmatmul_16x16(double *c, const double *a, const double *b,
unsigned long int m, unsigned long int n,
unsigned long int p);
void fmatmul_vec_16x16_slice_init();
void fmatmul_vec_16x16(double *c, const double *a, const double *b,
unsigned long int n, unsigned long int p);
#define MIN(a, b) ((a) < (b) ? (a) : (b))
/*void generate_random_matrix(double *matrix, int rows, int cols, double max_val) {
for (int i = 0; i < rows; ++i) {
for (int j = 0; j < cols; ++j) {
matrix[i * cols + j] = ((double)rand() / RAND_MAX) * max_val;
}

## Slide 13
}
}*/
void fmatmul_16x16(double *c, const double *a, const double *b,
unsigned long int M, unsigned long int N,
unsigned long int P) {
const unsigned long int block_size = 16;
unsigned long int block_size_p;
asm volatile("vsetvli %0, %1, e64, m1, ta, ma" : "=r"(block_size_p) : "r"(P));
for (unsigned long int p = 0; p < P; p += block_size_p) {
const unsigned long int p_ = MIN(P - p, block_size_p);
const double *b_ = b + p;
double *c_ = c + p;
asm volatile("vsetvli zero, %0, e64, m1, ta, ma" ::"r"(p_));

## Slide 14
for (unsigned long int m = 0; m < M; m += block_size) {
const double *a_ = a + m * N;
double *c__ = c_ + m * P;
fmatmul_vec_16x16_slice_init();
fmatmul_vec_16x16(c__, a_, b_, N, P);
}
}
}
void fmatmul_vec_16x16_slice_init() {
asm volatile("vmv.v.i v0, 0");
asm volatile("vmv.v.i v1, 0");
asm volatile("vmv.v.i v2, 0");
asm volatile("vmv.v.i v3, 0");
asm volatile("vmv.v.i v4, 0");
asm volatile("vmv.v.i v5, 0");
asm volatile("vmv.v.i v6, 0");
asm volatile("vmv.v.i v7, 0");
asm volatile("vmv.v.i v8, 0");
asm volatile("vmv.v.i v9, 0");

## Slide 15
asm volatile("vmv.v.i v10, 0");
asm volatile("vmv.v.i v11, 0");
asm volatile("vmv.v.i v12, 0");
asm volatile("vmv.v.i v13, 0");
asm volatile("vmv.v.i v14, 0");
asm volatile("vmv.v.i v15, 0");
}
void fmatmul_vec_16x16(double *c, const double *a, const double *b,
const unsigned long int N, const unsigned long int P) {
double t0, t1, t2, t3, t4, t5, t6, t7, t8, t9, t10, t11, t12, t13, t14, t15;
const double *a_ = a;
t0 = *a, a += N;
t1 = *a, a += N;
t2 = *a, a += N;
t3 = *a, a += N;
t4 = *a, a += N;
t5 = *a, a += N;
t6 = *a, a += N;

## Slide 16
t7 = *a, a += N;
t8 = *a, a += N;
t9 = *a, a += N;
t10 = *a, a += N;
t11 = *a, a += N;
t12 = *a, a += N;
t13 = *a, a += N;
t14 = *a, a += N;
t15 = *a;
asm volatile("vle64.v v16, (%0);" ::"r"(b));
b += P;
unsigned long int n = 0;
while (n != N) {
#ifdef VCD_DUMP
if (n == 8)
event_trigger = +1;
if (n == 12)
event_trigger = -1;
#endif

## Slide 17
t7 = *a, a += N;
t8 = *a, a += N;
t9 = *a, a += N;
t10 = *a, a += N;
t11 = *a, a += N;
t12 = *a, a += N;
t13 = *a, a += N;
t14 = *a, a += N;
t15 = *a;
asm volatile("vle64.v v16, (%0);" ::"r"(b));
b += P;
unsigned long int n = 0;
while (n != N) {
#ifdef VCD_DUMP
if (n == 8)
event_trigger = +1;
if (n == 12)
event_trigger = -1;
#endif

## Slide 18
a = a_ + ++n;
asm volatile("vfmacc.vf v0, %0, v16" ::"f"(t0));
t0 = *a, a += N;
asm volatile("vle64.v v17, (%0);" ::"r"(b));
b += P;
asm volatile("vfmacc.vf v1, %0, v16" ::"f"(t1));
t1 = *a, a += N;
asm volatile("vfmacc.vf v2, %0, v16" ::"f"(t2));
t2 = *a, a += N;
asm volatile("vfmacc.vf v3, %0, v16" ::"f"(t3));
t3 = *a, a += N;
asm volatile("vfmacc.vf v4, %0, v16" ::"f"(t4));
t4 = *a, a += N;
asm volatile("vfmacc.vf v5, %0, v16" ::"f"(t5));
t5 = *a, a += N;
asm volatile("vfmacc.vf v6, %0, v16" ::"f"(t6));
t6 = *a, a += N;
asm volatile("vfmacc.vf v7, %0, v16" ::"f"(t7));
t7 = *a, a += N;

## Slide 19
asm volatile("vfmacc.vf v8, %0, v16" ::"f"(t8));
t8 = *a, a += N;
asm volatile("vfmacc.vf v9, %0, v16" ::"f"(t9));
t9 = *a, a += N;
asm volatile("vfmacc.vf v10, %0, v16" ::"f"(t10));
t10 = *a, a += N;
asm volatile("vfmacc.vf v11, %0, v16" ::"f"(t11));
t11 = *a, a += N;
asm volatile("vfmacc.vf v12, %0, v16" ::"f"(t12));
t12 = *a, a += N;
asm volatile("vfmacc.vf v13, %0, v16" ::"f"(t13));
t13 = *a, a += N;
asm volatile("vfmacc.vf v14, %0, v16" ::"f"(t14));
t14 = *a, a += N;
asm volatile("vfmacc.vf v15, %0, v16" ::"f"(t15));
t15 = *a;
a = a_ + ++n;
if (n == N)
break;
asm volatile("vfmacc.vf v0, %0, v17" ::"f"(t0));
t0 = *a, a += N;

## Slide 20
// Load one row of B
asm volatile("vle64.v v16, (%0);" ::"r"(b));
b += P;
asm volatile("vfmacc.vf v1, %0, v17" ::"f"(t1));
t1 = *a, a += N;
asm volatile("vfmacc.vf v2, %0, v17" ::"f"(t2));
t2 = *a, a += N;
asm volatile("vfmacc.vf v3, %0, v17" ::"f"(t3));
t3 = *a, a += N;
asm volatile("vfmacc.vf v4, %0, v17" ::"f"(t4));
t4 = *a, a += N;
asm volatile("vfmacc.vf v5, %0, v17" ::"f"(t5));
t5 = *a, a += N;
asm volatile("vfmacc.vf v6, %0, v17" ::"f"(t6));
t6 = *a, a += N;
asm volatile("vfmacc.vf v7, %0, v17" ::"f"(t7));
t7 = *a, a += N;
asm volatile("vfmacc.vf v8, %0, v17" ::"f"(t8));
t8 = *a, a += N;
asm volatile("vfmacc.vf v9, %0, v17" ::"f"(t9));
t9 = *a, a += N;
asm volatile("vfmacc.vf v10, %0, v17" ::"f"(t10));
t10 = *a, a += N;

## Slide 21
asm volatile("vfmacc.vf v11, %0, v17" ::"f"(t11));
t11 = *a, a += N;
asm volatile("vfmacc.vf v12, %0, v17" ::"f"(t12));
t12 = *a, a += N;
asm volatile("vfmacc.vf v13, %0, v17" ::"f"(t13));
t13 = *a, a += N;
asm volatile("vfmacc.vf v14, %0, v17" ::"f"(t14));
t14 = *a, a += N;
asm volatile("vfmacc.vf v15, %0, v17" ::"f"(t15));
t15 = *a;
}
// Last iteration: store results
asm volatile("vfmacc.vf v0, %0, v17" ::"f"(t0));
asm volatile("vse64.v v0, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v1, %0, v17" ::"f"(t1));
asm volatile("vse64.v v1, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v2, %0, v17" ::"f"(t2));
asm volatile("vse64.v v2, (%0);" ::"r"(c));
c += P;

## Slide 22
asm volatile("vfmacc.vf v3, %0, v17" ::"f"(t3));
asm volatile("vse64.v v3, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v4, %0, v17" ::"f"(t4));
asm volatile("vse64.v v4, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v5, %0, v17" ::"f"(t5));
asm volatile("vse64.v v5, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v6, %0, v17" ::"f"(t6));
asm volatile("vse64.v v6, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v7, %0, v17" ::"f"(t7));
asm volatile("vse64.v v7, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v8, %0, v17" ::"f"(t8));
asm volatile("vse64.v v8, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v9, %0, v17" ::"f"(t9));
asm volatile("vse64.v v9, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v10, %0, v17" ::"f"(t10));
asm volatile("vse64.v v10, (%0);" ::"r"(c));

## Slide 23
c += P;
asm volatile("vfmacc.vf v11, %0, v17" ::"f"(t11));
asm volatile("vse64.v v11, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v12, %0, v17" ::"f"(t12));
asm volatile("vse64.v v12, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v13, %0, v17" ::"f"(t13));
asm volatile("vse64.v v13, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v14, %0, v17" ::"f"(t14));
asm volatile("vse64.v v14, (%0);" ::"r"(c));
c += P;
asm volatile("vfmacc.vf v15, %0, v17" ::"f"(t15));
asm volatile("vse64.v v15, (%0);" ::"r"(c));
}
void printnumb(double *numb, int rows, int cols) {
for (int i = 0; i < rows; i++) {
for (int j = 0; j < cols; j++) {
printf("%6.1f ", numb[i * cols + j]);
}
printf("\n");

## Slide 24
}
}
int main(){
double x[256] = {
48, 27, 31, 17, 46, 13, 28, 4, 49, 25, 41, 26, 32, 27, 13, 33,
18, 43, 42, 2, 47, 18, 42, 28, 17, 1, 5, 16, 28, 2, 25, 23,
27, 42, 27, 16, 40, 30, 14, 7, 7, 11, 36, 27, 43, 13, 31, 14,
22, 38, 22, 16, 30, 22, 38, 39, 30, 20, 45, 5, 12, 48, 40, 19,
4, 15, 31, 10, 48, 1, 14, 15, 30, 1, 2, 18, 16, 9, 31, 46,
18, 47, 47, 13, 1, 13, 10, 37, 41, 21, 12, 3, 26, 27, 29, 39,
34, 13, 40, 5, 20, 49, 23, 15, 23, 3, 45, 15, 11, 4, 9, 43,
2, 30, 5, 5, 18, 18, 1, 40, 17, 24, 42, 17, 25, 42, 16, 49,
41, 4, 7, 6, 10, 48, 6, 32, 16, 21, 6, 45, 39, 35, 3, 42,
48, 12, 13, 46, 21, 31, 2, 21, 43, 28, 36, 45, 17, 1, 24, 32,
38, 33, 43, 44, 46, 15, 22, 21, 3, 47, 3, 6, 12, 5, 15, 6,
37, 6, 27, 8, 48, 16, 32, 24, 37, 21, 28, 10, 32, 27, 17, 46,
36, 40, 39, 11, 34, 23, 18, 3, 1, 28, 38, 30, 29, 6, 28, 14,
9, 36, 48, 19, 7, 28, 15, 38, 1, 45, 38, 10, 28, 48, 33, 2,
43, 28, 26, 30, 5, 49, 17, 31, 30, 19, 31, 35, 4, 8, 16, 46,
4, 3, 3, 6, 20, 10, 8, 10, 16, 20, 8, 32, 18, 30, 42, 6 };

## Slide 25
double y[256] = {
48, 27, 31, 17, 46, 13, 28, 4, 49, 25, 41, 26, 32, 27, 13, 33,
18, 43, 42, 2, 47, 18, 42, 28, 17, 1, 5, 16, 28, 2, 25, 23,
27, 42, 27, 16, 40, 30, 14, 7, 7, 11, 36, 27, 43, 13, 31, 14,
22, 38, 22, 16, 30, 22, 38, 39, 30, 20, 45, 5, 12, 48, 40, 19,
4, 15, 31, 10, 48, 1, 14, 15, 30, 1, 2, 18, 16, 9, 31, 46,
18, 47, 47, 13, 1, 13, 10, 37, 41, 21, 12, 3, 26, 27, 29, 39,
34, 13, 40, 5, 20, 49, 23, 15, 23, 3, 45, 15, 11, 4, 9, 43,
2, 30, 5, 5, 18, 18, 1, 40, 17, 24, 42, 17, 25, 42, 16, 49,
41, 4, 7, 6, 10, 48, 6, 32, 16, 21, 6, 45, 39, 35, 3, 42,
48, 12, 13, 46, 21, 31, 2, 21, 43, 28, 36, 45, 17, 1, 24, 32,
38, 33, 43, 44, 46, 15, 22, 21, 3, 47, 3, 6, 12, 5, 15, 6,
37, 6, 27, 8, 48, 16, 32, 24, 37, 21, 28, 10, 32, 27, 17, 46,
36, 40, 39, 11, 34, 23, 18, 3, 1, 28, 38, 30, 29, 6, 28, 14,
9, 36, 48, 19, 7, 28, 15, 38, 1, 45, 38, 10, 28, 48, 33, 2,
43, 28, 26, 30, 5, 49, 17, 31, 30, 19, 31, 35, 4, 8, 16, 46,
4, 3, 3, 6, 20, 10, 8, 10, 16, 20, 8, 32, 18, 30, 42, 6 };
double zv[256] = {0};
fmatmul_16x16(zv, x, y, 16, 16, 16);
printf("\n");
printf("success!\n");
printnumb(zv, 16, 16);
return 0;
}

## Slide 26
output

## Slide 27
output for different cycles
Size | Executed Cycles | Wallclock Time | Simulation Speed(cycles/sec)
1*1 | cd7 | 1.445s | 2274.74
5*5 | 4be9 | 10.395s | 1869.46
16*16 | 77dd4 | 138.126s | 3554.46

## Slide 28
Work-let Name: CT006_RISC_V Vector Implementation of Channel Estimation and develop Custom vector Intrinsics of
Worklet Details
Worklet ID: CT006
College Name:Cambridge Institute of Technology Banglore
  Status and future plan
  The worklet progress is satisfactory based on the targets allocated
  Latest Literature Review
  Litereature Review on Channe Estinmation Based Matrix Muliplication
  Expert Insights
  Studied the algorithms.
  Any other comment
  Need to work on ARIANNA and optimization based on 1024.
Professor Comments (To be filled in and presented by professor (Either)
Date: 21-04-2025
COMPUTATION RESOURCE Details:
[Google Collab/ Kaggle / GPU from College lab with compute hours etc]